## Slide 1: Chap. 3 Data Representation
3-1 Data Types
  Binary information is stored in memory or processor registers
  Registers contain either data or control information
    Data are numbers and other binary-coded information
    Control information is a bit or a group of bits used to specify the sequence of command signals
  Data types found in the registers of digital computers
    Numbers used in arithmetic computations
    Letters of the alphabet used in data processing
    Other discrete symbols used for specific purpose
  Number Systems
    Base or Radix r system : uses distinct symbols for r digits
    Most common number system :Decimal, Binary, Octal, Hexadecimal
    Positional-value(weight) System : r2 r 1r0.r-1 r-2 r-3
      Multiply each digit by an integer power of r and then form he sum of all weighted digits

## Slide 2
  Decimal System/Base-10 System
    Composed of 10 symbols or numerals(0, 1, 2, 3, 4, 5, 6, 7, 8, 9, 0)
  Binary System/Base-2 System
    Composed of 10 symbols or numerals(0, 1)
    Bit = Binary digit
  Hexadecimal System/Base-16 System : Tab. 3-2
    Composed of 16 symbols or numerals(0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F)
  Binary-to-Decimal Conversions
1011.1012 = (1 x 23) + (0 x 22)+ (1 x 21) + (1 x 2o) + (1 x 2-1) + (0 x 2-2) + (1 x 2-3)
= 810+ 0 + 210 + 110 + 0.510 + 0 + 0.12510
= 11.62510
  Decimal-to-Binary Conversions
    Repeated division(See p. 69, Fig. 3-1)
    37 / 2 = 18 remainder 1 (binary number will end with 1) : LSB
18 / 2 = 9 remainder 0
9 / 2 = 4 remainder 1
4 / 2 = 2 remainder 0
2 / 2 = 1 remainder 0
1 / 2 = 0 remainder 1 (binary number will start with 1) : MSB
  Read the result upward to give an answer of 3710 = 1001012
  0.375 x 2 = 0.750 integer 0 MSB
    0.750 x 2 = 1.500 integer 1 .
    0.500 x 2 = 1.000 integer 1 LSB
  Read the result downward .37510 = .0112

## Slide 3
  Hex-to-Decimal Conversion
2AF16 = (2 x 162) + (10 x 161) + (15 x 16o)
= 51210 + 16010 + 1510
= 68710
  Decimal-to-Hex Conversion
42310 / 16 = 26 remainder 7 (Hex number will end with 7) : LSB
2610 / 16 = 1 remainder 10
110 / 16 = 0 remainder 1 (Hex number will start with 1) : MSB
  Read the result upward to give an answer of 42310 = 1A716
  Hex-to-Binary Conversion
9F216 = 9 F 2
= 1001 1111 0010
= 1001111100102
Table 3-2
Hex Binary Decimal
0 0000 0
1 0001 1
2 0010 2
3 0011 3
4 0100 4
5 0101 5
6 0110 6
7 0111 7
8 1000 8
9 1001 9
A 1010 10
B 1011 11
C 1100 12
D 1101 13
E 1110 14
F 1111 15
  Binary-to-Hex Conversion
1 1 1 0 1 0 0 1 1 02 = 0 0 1 1 1 0 1 0 0 1 1 0
3 A 6
= 3A616

## Slide 4
  Binary-Coded-Decimal Code
    Each digit of a decimal number is represented by its binary equivalent
8 7 4 (Decimal)
1000 0111 0100 (BCD)
    Only the four bit binary numbers from 0000 through 1001 are used
    Comparison of BCD and Binary
13710 = 100010012 (Binary) - require only 8 bits
13710 = 0001 0011 0111BCD (BCD) - require 12 bits
  Alphanumeric Representation
    Alphanumeric character set
      10 decimal digits, 26 letters, special character($, +, =,….)
    ASCII :
      Standard alphanumeric binary code.

## Slide 5
Complements
  Complements are used in digital computers for simplifying the subtraction operation and for logical manipulation.
  There are two types of complements for base r system
    1) r’s complement 2) (r-1)’s complement
      Binary number : 2’s or 1’s complement
      Decimal number : 10’s or 9’s complement
  (r-1)’s Complement
    (r-1)’s Complement of N = (rn-1)-N
      9’s complement of N=546700
      (106-1)-546700= (1000000-1)-546700= 999999-546700
      = 453299
      1’s complement of N=101101
      (26-1)-101101= (1000000-1)-101101= 111111-101101
      = 010010
  r’s Complement
    r’s Complement of N = rn-N
      10’s complement of 2389= 7610+1= 7611
      2’s complement of 1101100= 0010011+1= 0010100
N : given number
r : base
n : digit number
546700(N) + 453299(9’s com)
=999999
101101(N) + 010010(1’s com)
=111111
* r’s Complement
(r-1)’s Complement +1 =(rn-1)-N+1= rn-N

## Slide 6
  Subtraction of Unsigned Numbers
    1) M + (rn-N)
    2) M  N : Discard end carry, Result = M-N
    3) M  N : No end carry, Result = - r’s complement of (N-M)
      Decimal Example)
      72532(M) - 13250(N) = 59282
      72532
      + 86750 (10’s complement of 13250)
      1 59282
      Result = 59282
      Binary Example)
      1010100(X) - 1000011(Y) = 0010001
      1010100
      + 0111101 (2’s complement of 1000011)
      1 0010001
      Result = 0010001
(M-N), N0
      13250(M) - 72532(N) = -59282
      13250
      + 27468 (10’s complement of 72532)
      0 40718
      Result = -(10’s complement of 40718)
      = -(59281+1) = -59282
M  N
M  N
Discard End Carry
No End Carry
      1000011(X) - 1010100(Y) = -0010001
      1000011
      + 0101100 (2’s complement of 1010100)
      0 1101111
      Result = -(2’s complement of 1101111)
      = -(0010000+1) = -0010001
X  Y
X  Y

## Slide 7
Integer Representation
    Signed-magnitude representation
    Signed-1’s complement representation
    Signed-2’s complement representation
+14 -14
0 0001110 1 0001110
0 0001110 1 1110001
0 0001110 1 1110010

## Slide 8
  Arithmetic Addition
    Addition Rules of Ordinary Arithmetic
      The signs are same : sign= common sign, result= add
      The signs are different : sign= larger sign, result= larger-smaller
    Addition Rules of the signed 2’s complement
      Add the two numbers including their sign bits
      Discard any carry out of the sign bit position
  Arithmetic Subtraction
    Subtraction is changed to an Addition
      (± A) - (+ B) = (± A) + (- B)
      (± A) - ( - B) = (± A) + (+ B)
  Overflow
    Two numbers of n digits each are added and the sum occupies n+1 digits
    n + 1 bit cannot be accommodated in a register with a standard length of n bits.
(-12) + (-13) = -25
(+12) + (+13) = +25
(+25) + (-37)
= 37 - 25 = -12
*Addition Exam)
+ 6 00000110 - 6 11111010
+ 13 00001101 + 13 00001101
+ 19 00010011 + 7 00000111
+ 6 00000110 - 6 11111010
- 13 11110011 - 13 11110011
- 7 11111001 - 19 11101101
* Subtraction Exam) (- 6) - ( - 13) = +7
11111010 - 11110011 = 11111010 + 2’s comp of 11110011
= 11111010 + 00001101
= 1 00000111 = +7
Discard End Carry

## Slide 9
  Overflow
    An overflow may occur if the two numbers added are both positive or both negative
      When two unsigned numbers are added
        an overflow is detected from the end carry out of the MSB position
      When two signed numbers are added
        the MSB always represents the sign
        - the sign bit is treated as part of the number
        - the end carry does not indicate an overflow
* Overflow Example)
out in out in
carries 0 1 carries 1 0
+ 70 0 1000110 - 70 1 0111010
+ 80 0 1010000 - 80 1 0110000
+ 150 1 0010110 - 150 0 1101010

## Slide 10
3-4 Floating-Point Representation
  The floating-point representation of a number has two parts
    1) Mantissa : signed, fixed-point number
    2) Exponent : position of binary(decimal) point
  Scientific notation : m x re (+0.6132789 x 10+4)
    m : mantissa, r : radix, e : exponent
  Example : m x 2e = +(.1001110)2 x 2+4
  Normalization
    Most significant digit of mantissa is nonzero
* Decimal + 6132.789
Fraction Exponent
+0.6132789 +4
Fraction Exponent
01001110 000100

## Slide 11
3-6 Error Detection Codes
  Binary information transmitted through some form of communication medium is subject to external noise
  Parity Bit
    An extra bit included with a binary message to make the total number of 1’s either odd or even.
  Even-parity method
    The value of the parity bit is chosen so that the total number of 1s (including the parity bit) is an even number
    1 1 0 0 0 0 1 1
  Odd-parity method
    Exactly the same way except that the total number of 1s is an odd number
    1 1 0 0 0 0 0 1
Transmitter
Receiver
~
~

Added parity bit
Added parity bit